## Slide 1
Slice on demand API Proposal

## Slide 2: Why Slicing Use Cases
5G Equipment Industry Slicing
5G Electric Slicing
5G Auto Driving
Live Streaming
Assurance Levels Required
Upstream Assurance
Downstream SLA Assurance
Plenty of End Devices Access
Wide Area Low Latency
Isolated and Dedicated Network Resources
Remote Control Low Latency
High Availability and Stability Required
Isolated and Dedicated Network Resources
Downstream SLA Assurance
Mature Fields
New Potential Valued Fields
Reason 1: Static Slicing has helped operators monetized. Dynamic Slicing is on the way of huge potential value. It’s about the time to promote slicing.

## Slide 3: Why Slicing in CAMARA?
Reason 2: Utilize the CAMARA platform to fasten the operator monetization of Slicing.
Closer and more directly to Developers and Customers.
Attract more player jointly speed up the development of Slice.
Dynamic Slicing is suitable to be designed as Service APIs for users to call again and again, within Open API Platform.

## Slide 4: For QoS guaranteed scenarios，Network slicing is the hottest solution
QoS Guaranteed Requirements
With the development of streaming, cloud games, VR/AR, auto driving, there appears emerging requirements for stable network quality, even under the high load scenario.
Network Slice is the hottest topic in 5G to provide differentiate and guaranteed connectivity by isolate resource and mechanism. Dynamic slicing can provide flexible service possibility to different industry by the automatic orchestration and management.
Network slicing is the common consensus of Europe operators
Carrier network
Slicing Infrastructure
Slicing Service Operation
Slicing Instance Management
UE
TN
AN
CN
Slicing KPI monitoring
Slicing ordering
Slicing user management
slicing terminal monitoring
APP
Server
slicing service monitoring
Open API
Tenant Service Platform
3
4
1
2
Cloud Gaming
Live Broadcast

## Slide 5: Two monetization paths of network slicing for operators
Standard Service Products with Dynamic Slicing
Deterministic latency
Deterministic bandwidth
Security isolation
Complex service scenarios
…
Standard slice package
Self-service provisioning
Common requirements with same services
…
Path 1:
For High-value Large Enterprises
Path 2:
For Massive B2B2C/2C Oriented SME
Network Slicing
Monetization
Provisioning
Monitoring
Management
Assurance
Dedicated & Customized Network with Static Slicing
Slice Products
Mature
Most popular in Europe Market

## Slide 6: We propose Slice on demand API to exposure the operator’s dynamic slicing capability
API Exposure Gateway
Gaming APP1
Gaming APP2
Gaming APP N…
Gamer1
Gamer2
Gamer3
Gamer4
Gamer N..
Slice#1
For Gamer1 and Gamer2
Slice#2
For Gamer3
Slice#4
For Gamer5
Gamer5
Operator network
Slice on demand API
Network capability ready for Dynamic Slicing
Take cloud gaming service as example:
Gamer:
Request a QoS guarantee service
Pay for each success request
Slice#3
For Gamer4
Gaming APP:
Invoke slice on demand API to get most suitable slice for dedicate gamer to provide guaranteed QoS
Pay for each success invocation
Operator:
Exposure slice on demand API via API gateway to gaming APPs, to simple the developers invocation
Provide dynamic slicing capabilities including slice provisioning, slice SLA prediction, slice SLA monitoring and assurance capabilities
Automatic orchestrate the slice lifecycle management
Slice provision, user subscription, SLA prediction, slice termination ….
Service API
Network API

## Slide 7: The implement proposal
RAN Management Domain
Enterprise Customer
Evaluate SLA can be guaranteed
① Slice on demand API
（Service time、Service location、Service SLA Targets）
Evaluate whether the SLA can be met
gNodeB
② RAN Slice SLA Prediction API
Guaranteed or not
N
⑤ Notify the user that the request is successful.
Y
③ Notify the user and refuse the request
Provision Slice
Network Platform
（Open Gateway/
CSMF/NSMF）
Network
Resource
Service API
Network API
RAN Management Domain
gNodeB
RAN slice resource provisioning
5GC Management Domain
Core slice resource provisioning
5G Core
④Slice LCM API(provision, subscription, deactivation…)

## Slide 8: The API definition proposal
API Name | Slice on demand API
Description | Predict the SLA can be guaranteed or not for the indicated time and location, and provide resource reserved network slice to guarantee the service QoS
Input Parameters | Service Time：Start Time ~ End Time
 | Service Location：longitude & latitude
 | SLA Targets：Counters and Values（such as DL/UL Avg Throughput, Latency）
Return Results | Slice SLA can be guaranteed or not(Y/N) Slice ID will be used to guarantee the user requirement
Service API
RAN Network API
API Name | RAN Slice SLA Prediction API
Description | Pre-evaluate whether the RAN network SLA target can be guaranteed
Input Parameters | NSSAI：Slice ID
 | Service Time：Start Time ~ End Time
 | Service Location：longitude & latitude
 | SLA Targets：RAN Counters and Values（such as DL/UL Avg Throughput, Latency）
 | Constraints: For example, consider background MBB UEs and the maximum number of RBs reserved for slicing
Return Results | Required RB resources, QoS parameters RAN network SLA target can be guaranteed or not
API Name | RAN LCM API
Description | Manage the slice allocation, deallocation, Slice KPI monitoring, with the RAN dynamic resource reservation capability
Return Results | RAN Slice ID can be used

## Slide 9: SLA prediction is important for QoS guarantee services
New Slice
Slice#1
APP#1
Slice SLA Prediction API
APP#2
Slice SLA Prediction API
Existing user
New user
Scenario1: Evaluate the existing slice can meet the new user QoS requirement or not
Scenario2: Evaluate the network slice resource needed to meet the new users QoS requirement

## Slide 10: Summary
Network Slicing is the best way to monetize to network for different service requirement. It is becoming the hottest topic in standards organization and telecom industry
Most of the operators in the world are practicing the network slicing. Dynamic slicing is becoming the common consensus and is growing mature.
For the massive market of different SMEs and services, exposure the dynamic slicing capability via a simple and standard API to developers is the most efficient way to expand the markets
We propose to discuss the Slice on demand API family requirement and definition in CAMARA community and GSMA Open Gateway, which can help operators to accelerate the network slice monetization and let more developers can use the network slice in a easier way

## Slide 11: Input/output params of the API proposal (ref Page 8 Service API)
Input Parameters:
  Service Time：Start Time ~ End Time
  Service Area：Geographical area (Point, Line, Area)
  Guaranteed terminals：Number of terminals
  SLA Targets：SLA KPIs (such as DL/UL Avg Throughput, Latency)
Output Parameters:
  Slice Reservation Result： network slice reservation success (with Slice ID) or failure
An example: a developer may use this API to book a network slice with expected service time, expected service area, expected guaranteed numbers of terminals and expected SLA targets for 2 hours to 2 weeks in advance for some scheduled events like a live stream festival scheduled in some place.

## Slide 12: Comparison with QoD API and Site-to-Cloud VPN API
Aspects | Quality on Demand | Network slicing API | Site-to-Cloud VPN API
Targeting customers | The QoD API offers the application developers the capability to request for stable latency (reduced jitter) or throughput for some specified application data flows between application clients (within a user device) and Application Servers (backend services). The developer has a pre-defined set of Quality of Service (QoS) profiles which they could choose from depending on their latency or throughput requirements. | Cloud-gaming, AR/VR, Live Video Streaming, Real-time Multi-Media etc through mobile networks A typical example case is to call this API for a live video show scheduled several days later, the requested slice servicing duration may be several hours and only focuses on some specific location (like a stadium for the live show). This is not like the case of QoD API usually to upgrade the performance of a (collection of) ongoing QoS flows. | industries, finance, education, medical, Internet of things, cloud desktop, cloud conference, cloud recording and etc The customers usually use this API to establish a VPN not just only lasting for several hours like the network slicing API cases.
Usage of the API | The usage of the API is based on QoS session resources, which can be created (based on available QoS profiles), queried and deleted. The deletion of a requested session can be triggered by the API consumer or can be triggered automatically. The automatic process is triggered either when the requested specified duration of a QoS session has reached its limit or the default session expiration time has been reached (within an example provider implementation it is set to 24hrs). QoD API allows the 3rd party (could be B2C or B2B) to upgrade the performance of a (collection of) ongoing QoS flows. The actual network solution that operator uses to fulfil this upgrade (SD-WAN, network slicing, DNN/APN provisioning...) should remain transparent to the 3rd party. The 3rd party is only interest in getting this request fulfilled, no matter what is the network solution used for that end. If the operator decides to use network slicing, this is somewhat related to the model that 3GPP acknowledges as "Network Slice as NOP internals" | reserve, dynamically provisioning, query, dynamically destroy a slice with customized SLA assurance capabilities, customized service duration, expected slice covered locations. Network slicing API allows the 3rd party (likely B2B) to ask for the allocation of dedicated resource capacity. This is somewhat related to the model that 3GPP acknowledges as "Network Slice as a Service". This model offers the flexibility for operator offer to a particular customer a dedicated network slice as a product. This product will carry all PDU connectivity services as the customer requires, potentially towards different DNNs (e.g., local breakout in the tenants computing centre, public voice to IMS, and towards public internet), while each PDU connectivity service might carry multiple QoS flows of different QoS. | when someone calls the API service with network SLA requirements, telecom operators can create non-public cloud leased network service by orchestrating the IP VPN connections of metropolitan network and/or backbone network.
Level of isolation/Security | QoD API, which based on QoS session resources, cannot discriminate and differentially treat the same type of traffic (e.g. VoIP traffic) coming from different sources, while if same type of traffic is assigned to different slices via using Slice API, it can be discriminated and treated differently. | Slice API provides customers dedicated, isolated network resources as a complete end-to-end virtual network for a given source. No existing QoS-based solution can offer anything like that. QoD API, which based on QoS session resources, does not have the ability to perform traffic isolation. For example, to support the IoT traffic from a V2X health monitoring network (e.g. connecting hospitals and outpatients) which typically has strict privacy and security requirements, Slice API can be used to reserve a specific slice for that. Usually over shared PLMN infrastructure | Higher
Utilized technology | 4G/5G | 5G/MBB | 4G/5G/FBB orchestrating the IP VPN connections of metropolitan network and/or backbone network.

## Slide 13: Some clarifications to other comments raised by companies during the discussion
Q: Naming (The API should NOT mention slicing, this is because the realisation might be other than a slice, especially when not on 5G. Why not "connectivity management" or "resource management". The commitment level when reserving connectivity or resources should be high, but CSP determined.)
A: I am not against investigating a more general idea not focusing on 5G via other activities in CAMARA further. But here, the purpose of this proposal is really targeting on the slicing which is a key feature of 5G and accepted by the verticals to buy as a service (3GPP acknowledges this as "Network Slice as a Service"). As you see from the previous discussion (#333 (comment) from operator China Unicom reply as "An API is a product, for operators, we believe slice can be sell as a product as well. Slice may provide customers dedicated, isolated network resources. From application scenario, end API consumers, price and billing". If CAMARA can provide such API towards 3rd party (like B2B), then it will offer the flexibility for operators to offer to a particular customer a dedicated network slice as a product. As I explained here (#317 (comment)):
  A developer may use this user-friendly API to book a network slice with expected service time period, expected service area, expected guaranteed numbers of terminals and expected SLA targets in advance (e.g. 2 hours or 2 weeks in advance) for some planned event like a live video streaming show scheduled in some place during some time period.
  The Network slicing API allows Operators/CSPs to offer dedicated resources to different tenants (as B2B customers) via the Network slice as a Service. This is a kind of commodity and business monetization opportunities for operators to sell on-demand slice service to third-party tenants.

## Slide 14: Some clarifications to other comments raised by companies during the discussion
Q: The API should contain a time range (e.g. start time / stop time) and a location range (Geo Area) and a desired connectivity performance (e.g. throughput, approximate number of devices, etc)
A: yes, I agree with that very much. This aligns with the input of this API.
Q: The API should not dictate how the reserved capacity is used unless this is needed and influences the network preparation, Maybe the APIs should indicate a “max possible” capacity.
A: yes, I agree that the API should not dictate how the reserved capacity is used unless this is needed and influences the network preparation. This API is a user-friendly API which should only express the service requirements from the customers point of view (just as "What"). If it is confirmed successfully by the operators as a slice reservation result, I think then the asked service requirements need to be ensured, otherwise how the operator can get the payment from the customers? :) I think this is quite similarly like the case of hotel room booking: the hotel service providers need to ensure the rooms are available for customers to be checked-in later after the room reservations done successfully by the customers. :)
Q: The API should not include target MSISDNs, in my view this is a separate API (in the same workgroup) to connect/disconnect devices to the reserved resources.
A: yes, I think no intention for this API to include the "target MSISDNs" uniquely identifying the mobile users. In the Input parameters of this API, it is just "Guaranteed terminals: Number of terminals" which means the "approximate number of devices".

## Slide 15
Thank you