## Slide 1: UE identifiers

## Slide 2: Abstract
This contribution analyzes GPSI, AF-specific External Identifier, and their availability for identifying a subscription (SUPI) in Camara APIs.
Based on the discussion, Ericsson proposes a way forward.

## Slide 3: Generic Public Subscription Identifier (GPSI)
GPSI is defined in 3GPP TS 23.501 clause 5.9.8 and 23.003 clause 28.8.
    Generic Public Subscription Identifier (GPSI) is needed for addressing a 3GPP subscription in different data networks outside of the 3GPP system. The 3GPP system stores within the subscription data the association between the GPSI and the corresponding SUPI.
The GPSI has two possible formats:
  An MSISDN (defined in 3GPP TS 23.003 clause 3.3)
      Example: 1555123456
  An External Identifier (defined in 3GPP TS 23.003 clause 19.7.2)
        The External Identifier shall have the form username@realm as specified in clause 2.1 of IETF RFC 4282
      Example: 1AD4G@subdomain.example.com
      Several external identifiers may be used for referring to the same subscription (SUPI).
Structure of the MSISDN

## Slide 4: External Identifier format of GPSI
3GPP TS 23.003:
  The External Identifier shall have the form username@realm as specified in clause 2.1 of IETF RFC 4282
  The username part format of the External Identifier shall contain a Local Identifier as specified in 3GPP TS 23.682 [98]. The realm part format of the External Identifier shall contain a Domain Identifier as specified in 3GPP TS 23.682 [98]. As specified in clause 4 of IETF RFC 4282 [53], the Domain Identifier shall be a duly registered Internet domain name. The combination of Local Identifier and Domain Identifier makes the External Identifier globally unique.
3GPP TS 23.682:
  Domain Identifier: identifies a domain that is under the control of a Mobile Network Operator (MNO). The Domain Identifier is used to identify where services provided by the operator network can be accessed (e.g. MTC-IWF or SCEF provided services). An operator may use different domain identifiers to provide access to different services and/or MTC Service Providers.
  Local Identifier: Identifier used to derive or obtain the IMSI. The Local Identifier shall be unique within the applicable domain. It is managed by the Mobile Network Operator.
  NOTE 1: Use of External Identifiers is not restricted to MTC only.

## Slide 5: AF-specific UE external identifier
AF-specific UE external identifier is just an GPSI in the format of an External Identifier, that happens to be specified for an AF, with the regular format of an External Identifier:
          <localIdentifier>@<AF-specific-domainRealm>
The AF-specific UE external identifier is associated to the SUPI in UDM/UDR.
  And is assumed that the MNO provisions it in UDM/UDR.
The AF-specified UE external identifier was introduced in Rel-17 to solve these problems:
  A UE may change its UE IP address when it is served by an Edge Computing site.
  If the AF identifies the UE with its UE IP address, the AF may lose control when the UE IP address changes.
  Due to privacy reasons the user may not want to disclose its MSISDN or External ID to the AF.
    If the user has disclosed its MSISDN or External ID to the AF, there is no need for AF-specific UE external ID.
The AF keeps the AF-specific UE external identifier for the duration of the AF session.
  The AF must not keep a binding to the UE IP address, since the UE IP address may change.
The AF specific UE external identifier must not contain an MSISDN, due to privacy reasons.

## Slide 6: AF obtaining the AF-specific UE external identifier
A new Nnef-UEId_Get service was introduced in Rel17
AF may invoke a new Nnef_UEId_Get service operation, enabling an AF to get the AF-specific UE external identifier for a given UE IP address. (see figure)
AF may also obtain the AF-specific UE external identifier in a response to any of these service operations.
  Nnef_EventExposure_Subscribe (Monitoring Events)
  Nnef_ParameterProvision_Create
  Nnef_ParameterProvision_Update
  Nnef_ParameterProvision_Get
After obtaining it, the AF may use the AF-specific UE external identifier in subsequent requests where a GPSI is used for identifying the UE.

## Slide 7: NEF obtaining a SUPI from a UE IP address
If NEF receives a request for a UE, identified by its UE IP address, NEF may obtain the SUPI of the UE prior to contacting 5GC NFs.
  … prior to executing a 5G Core operation based on SUPI (step 7 in the figure).
Response (step 8) may contain a GPSI of the UE, but not a SUPI.
Source: TS 23.502 clause 4.15.3.2.13

## Slide 8: Conclusion
How does the AF initially identify a UE?
An AF may identify the UE with its UE IP address, as seen from the AF.
The AF may get the GPSI out of band.
    Example: the AF may also have been provisioned, by the user or the AF, with its MSISDN. The user might have “logged” into the AF server, in which case, the AF already knows the MSISDN of the UE.
The AF may also get a GPSI in the format of AF-specific UE Identifier by querying NEF or in response to certain services, where the request uses the UE IP address.
The NEF may resolve the UE IP address to a SUPI prior to executing a 5GC operation.
It seems that use cases exists for using GPSI in any of the possible formats.

## Slide 9: Proposal
It is proposed that Camara enables AFs identifying the UE primarily with:
  A GPSI represented in any of the possible existing formats.
And secondary (optionally) with:
  The UE IP address or MAC address (together with the AF Identifier)
We believe that this covers all possible use cases.

## Slide 10: References
3GPP TS 23.501 5.20
3GPP TS 23.502 4.15.10, 4.15.3.2.13, 5.2.6.27
3GPP TS 23.003 19.7.2
NOTE: Stage 3 specifications are not yet created.
NOTE: Privacy aspects should be considered in 3GPP TS 33.501 but are not there yet.