## Slide 1
Network Slicing API Proposal
China Unicom, China Telecom

## Slide 2
For Slicing Scenarios, A New Slicing API Is Recommended
QoD API
Network Slicing API
QoS Requirements
Different scenarios have different requirements for QoS assurance. The difference is not only about SLA (throughput or latency or other KPIs), but also about the timing of assurance. For Example：
Cloud Gaming
Live Broadcast
Use cases
Single consumer | Multi enterprise users
Take effect immediately | Make a booking in advance (e.g. 1~2weeks)
Focus on latency and downlink throughput | Focus on Uplink throughput
Key
Requirements
Solution
For immediate effective mode
Only provide prioritized capability
Key KPI parameters:
  UE info
  Duration(xx seconds)
  QoS Level
For reserve effective mode
Provide QoS guaranteed capability
Key KPI parameters:
  Time Period(start~end)
  Region(point/line/area)
  UE Number(one or more)
  SLA KPI
CSP can evaluate network capabilities and reserve a slice service in advance based on slicing

## Slide 3: Background
With the development of streaming, cloud games, VR/AR, auto driving, there appears emerging requirements for network quality, especially under high throughput scenario. Network Slicing can better meet this need.
So we propose Network Slicing API, which can allow users to book a slice network service, under customized location within customized duration.

## Slide 4
Automatic Slice Management and Assurance Capabilities to Support Network Slicing Scenario
Other Domain
RAN Domain
OpenGateway/CSMF/NSMF
Slice SLA
Pre-Evaluation
Slice Provision
Automatic provisioning in minutes
Evaluate whether the SLA is met
Service API
Network API
Application
② Provision
③ SLA Monitoring
① Pre-Evaluation
Monitoring and RCA
Slice-level Monitoring
Monitoring Network APIs
Provision Network APIs
Pre-Evaluation Network APIs
Network Slicing Pre-Evaluation API
Network Slicing On Demand API
Network Slicing Monitoring API

## Slide 5: SLA Network Slicing, Based on Network Slice
Management Plane
5G RAN
③ NaaS Platform
Application
External API Gateway
Slice
① New API: Network Slicing APIs
Transformation Function
Internal API Gateway
Service API
NaaS Platform
Network API
3GPP Standard
② Netwrok API: Slice PreEvaluation API
Slice On Demand API
Slice Monitoring API
User Subscription
Slice Pre-Evaluation/On Demand /Monitoring
Control Plane
5G Core
UDM
PCF
③ Core Network User Subscription
UDM：ADD NFSNSSAI、ADD SNSSAI、ADD SMDATA
RAN Management Domain

## Slide 6
Slice Provisioning Workflow：About Network Slicing, 6 Steps
RAN Management Domain
End User （Live Streaming）
Evaluate Slice Service Request
① Get an Slice Service Assurance（2 Hours - 2Weeks in Advance)
Evaluate the RAN SLA Assurance
gNodeB
② Pre-evaluation
If can be assured
N
⑤ Notify User，Order Success
Y
③ Notify User, or Cancel Reservation
④ Subscribe, Bind User and Slice ID
5G Core
User Subscription
NaaS+BSS+OSS
Network Resource
Service API
Network API

## Slide 7: Reservation API：Service API With Network API
API Name | Network Slicing Pre-Evaluation
Function | Make SLA Reservation 2H – 2 Weeks in Advance
Input | Assurance Duration：Start From – To
 | Assurance Location：Enum（Point - Longitude and latitude ; Line – Array of Longitude and latitude ; Plane – Central Point and Radius）
 | Assurance Terminal：x Terminals
 | SLA Target：Upstream, Downstream, Latency
Output | Success / Fail（Y/N）
Service API
Network API
API Name | Slice Pre-Evaluation API
Function | Evaluate Whether SLA can be Assured
Input | Assurance Duration：Start From – To
 | Assurance Location：Enum（Point - Longitude and latitude ; Line – Array of Longitude and latitude ; Plane – Central Point and Radius）
 | Assurance Terminal：x Terminals
 | SLA Target：Upstream, Downstream, Latency
 | Restricted Conditions：eg. Considering MBB user, set the reserved upper limit for slice RB
Output | Assured or Fail, How much can be assured Cell RB Resources（%）

## Slide 8: Enable and Delete Slice Work Flow：Before and After the Assurance, CSMF/NSMF will Enable/Delete the Slice
RAN Management Domain
End User （Live Streaming）
Enable the Slice
After the assurance starts, the UE sends a registration request with the pre-allocated NSSAI through signaling. After the registration is successful, slice-level SLA assurance starts.
RAN Resource Creation
gNodeB
① Enable the Slice in RAN
RAN Resource Deletion
After Assurance, Delete the Slice
③ Delete the Slice
Network Resource
Service API
Network API
Under Assurance
② RAN Slice Resource Configuration
④ RAN Slice Resource Configuration Deletion
Core Network Management Domain
5G Core NEs
Core Slice Resource Creation
Core Slice Resource Deletion
Noted：Slice Creation and Deletion Network APIs are based on 3GPP
NaaS+BSS+OSS

## Slide 9
Thank you